## Slide 1
JETRACER SOCCER LEAGUE
STUDENTS: JAROD MARSHEL, ARJUN SIMHA, K GUPTA, COOPER RITTER,
CASEY RITTENHOUSE, JULIE HAM, MASON KANG
ADVISERS: Dalton Smith, Pete Sulcs, James Waltner, Prof. John Raiti, Amisha Somaiya
Construct JetRacer cars to compete in autonomous 2v2 soccer.
Incorporate a new sensor suite to enhance car capabilities and situational awareness.
Demonstrate the ability to score goals by dribbling and striking the ball in a controlled trajectory.
Enable cooperation with allies to score goals and oppose foes trying to score.
Jetson Orin Nano Developer Kit
  8 GB DDR5
  40 TOPS
  1.5GHz
                ZED2 Stereo AI Camera
  120° Wide-Angle FOV
  Neural Depth/Spatial Object Sensing
  Built-in IMU
                Tamiya TT-02 RC Chassis Kit
  Mabuchi RS-540 Brushed Motor
  Futaba S3004 Servo
  7V 3000mAh NiCd Battery Pack
  RS304 Receiver
  T3PV FM Controller
                PCA9685 Adafruit 16-Channel I2C Servo Driver
                Pololu 4-Channel RC Servo Multiplexer
                Miuzei 25kg High Torque Servo
                Anker Nano 10,000mAh Portable Charger
Roboflow computer vision software used to create image dataset.
  Annotated over 1000 images of cars, ball, goals, and crosses for dataset.
YOLO object detection algorithm allows for smooth integration with ZED2 and ROS.
  Utilized YOLOv8 model to improve both detection accuracy and inference speed.
Increased confidence rates of object detection by +20% compared to last year.
Achieves 30 FPS detection for 720p HD video stream.
Streamlined communication between distinct hardware and software processes using a ROS Noetic environment.
The top-level JetRacer package uses the ZED2 ROS wrapper for object detection to determine strategy.
Constructed a brand new 20' x 15' soccer arena.
Red and blue colored goals for object detection.
Assembled using 3D printed brackets and foam board.
Included cross symbols on the walls to assist with offensive and defensive soccer strategy.
Match played with a size 1.5 black and white soccer ball.
The Strategy node allows for simple node switching based on the environmental situation.
The FSM within the Strategy node transitions states based on detected objects and position, triggering or stopping individual movement nodes.
Each movement node uses CV information to determine proper trajectory and speed.
Demonstrated working 1v1 soccer with autonomous JetRacer agents.
            Improved sensor suite with ZED2 AI stereo camera.
  Enhanced object detection confidence using a new dataset.
  Implemented depth sensing and positional tracking.
  Increased perception capabilities using a swiveling servo camera mount.
            Created a more robust control strategy using a custom ROS Noetic package.
  Strategy FSM for offense and defense node switching.
  Flexible structure optimized for smooth future integrations.
            Upgraded JetRacer car hardware and mounts.
            Constructed a new soccer field.
            Provided detailed documentation for future years.
Future Work:
        Purchase hardware to construct additional cars.
        Utilize more ZED2 built-in capabilities.
        Improve strategy to include more environmental scenarios.
        Decrease object detection latency.
        Implement additional sensors, such as motor encoders, to supplement ZED2 IMU.
        Develop reinforcement learning in a simulation environment to train agents.
        References:
[1] “NVIDIA-AI-IOT/jetracer,” GitHub, Apr. 23, 2021. https://github.com/NVIDIA-AI-
IOT/jetracer (accessed May 17, 2024).
[2] B. L. M. de Oliveira, “bryanoliveira/soccer-twos-env,” GitHub, Apr. 12, 2024.
https://github.com/bryanoliveira/soccer-twos-env (accessed May 17, 2024).
Overlays detected objects bounding boxes over 3D point cloud for accurate object depth estimation and positional tracking.
Achieves a median error of 0.914% for depth measurements less than 5m.
Fig 1. Hardware CAD
Fig 2. Wiring Diagram
Fig 6. Positional Tracking
Fig 7. 3D Point Cloud of Detected Objects
Fig 9. Strategy Finite State Machine
Fig 4. Object Detection Validation Dataset
  Fig 5. Confusion Matrix of Test Data
Objectives
Object Detection
JetRacer Hardware
ROS Integration
85
154
123
89
176
1
1
1
3
1
5
3
2
8
1
160
140
120
100
80
60
40
0
20
blue goal
blue goal
car
cross
red goal
ball
background
car
cross
red goal
ball
background
True
Predicted
Depth Sensing & Positional Tracking
Field Design
Fig 8. JetRacer Soccer Field
Fig 3. JetRacer Package RQT Visualization
Soccer Strategy
Results
Future Work & References
Github Repository:
Notes: Horizontal Version